## Slide 1: Nigeria Electricity System Analysis (2000–2024)
Prepared by: Suleiman Taiwo – Energy Data & Metering Analyst
Date: December 2025
Trends, Emissions, Renewable Share & Decarbonization Outlook

## Slide 2: Executive Summary
Nigeria’s electricity sector is becoming more fossil-heavy, less renewable, and more carbon-intensive. This analysis evaluates two decades of data (2000-2024) to understand whether Nigeria is on track with her Energy Transition Plan (ETP) TOWARDS 82% renewables and 277 GW installed capacity by 2060
Renewable Energy
Renewable share dropped from 38% → 23%
(2000–2024),
while fossil share increased from 62% → 77%.
Electricity carbon intensity
Electricity carbon intensity remains relatively high, contributing significantly to national GHG emissions.
To meet the Nigeria Energy Transition Plan (ETP) pathway, Nigeria must rapidly scale renewable capacity, expand grid infrastructure, and accelerate investment into clean energy, storage, and hydrogen.
Net decarbonization index
Decarbonization index declined from –23% → –60%, reflecting accelerated dependency on gas-based generation.

## Slide 3: CONTEXT & PURPOSE
Why this analysis matters
1. Increase Fossil Dependance
Nigeria’s electricity sector faces three strategic challenges:
Fossil share rising instead of falling (2000-2024).
These trends conflict with the ETP’s target of 82% renewable capacity by 2050 and a 6.5× increase in electricity generation by 2060
Carbon intensity remains above 500–550 gCO₂/kWh, raising electricity emissions.
3. High and Variable Carbon Intensity
Hydro and other renewables not growing fast enough.
2. Declining Renewable Share

## Slide 4: Electricity MIX TREND
Renewables ↓ Fossils ↑ (2000–2024)
Fossil sources account for over 80% of total generation
Limited progress toward solar and hydro targets outlined in Nigeria’s Energy Transition Plan.

## Slide 5: Renewable Category
Hydro growth has remain stagnant
With no significant new capacity in two decades.

## Slide 6: Renewable Mix
Hydro remains the only major renewable.
Solar/wind adoption at grid-scale remains negligible.

## Slide 7: Decarbonization Index
Between 2000 and 2024, Nigeria’s electricity mix shifted
heavily toward fossil fuels, producing a DECARBONIZATION
chart trend that shows a steady deepening decline
(–23% to –53%).
Nigeria is moving in the opposite direction of global trends

## Slide 8: GreenHouse Gas Emission
A steady climb in GreenHouse Gas emission going in opposite direction of global trend

## Slide 9: 2024 Reality Check
Metric | Nigeria 2024 | ETP Target | Gap
Renewable share | 23 % | 82 % by 2050 | −59 %
Installed capacity | ~15 GW | 277 GW by 2060 | −262 GW
Solar PV | < 2 GW | 209 GW by 2060 | −207 GW
Hydro | ~ 2 GW | 11 GW by 2060 | −9 GW
BESS Storage | ≈ 0 GW | 130 GW by 2060 | −130 GW
Hydrogen | 0 GW | 36 GW by 2060 | −36 GW
Battery Energy Storage System (BESS)

## Slide 10: Recommendations
1. Scale Up Renewables
Accelerate solar PV & hydro to reverse decline.
2. Invest in Storage & Grid Modernization
Start Deployment of BESS and Green hydrogen at national level.
3. Loss reduction
Enhance smart metering rollout to reduce losses and improve consumption tracking
4. Strengthen Policy & Finance
Nigeria has made policy, regulatory, and market strides toward a cleaner energy future, but implementation gaps remain, especially for solar, wind, and bioenergy
Pathways to a More Efficient Energy Future

## Slide 11: Resources and Tools
Sources
Our World in Data – Energy Dataset
Nigeria Energy Transition and Investment Plan Update (2024)
Global Practice Guides — Renewable Energy (Nigeria)
Energy 2025 Guide
Tools
Python (Pandas)
SQL (PostgreSQL)
Power BI

## Slide 12: Contact
📧 Email
Suleyimantaiwo@gmail.com
🔗 LinkedIn
https://www.linkedin.com/in/suleimantaiwo/
💻 GitHub
https://github.com/SuleimanTaiwo/Nigeria-Electricity-System-Analysis.git
🌍 Portfolio Website
https://suleyimantaiwo.wixsite.com/portfolio